## Slide 1
Finite Element Method
Ron Timothy Gitonga Ndwiga, Esther Mugure Ngugi
LOGO HERE
Finite Element Method
Numerical Methods
Ron Timothy Gitonga Ndwiga
Esther Mugure Ngugi
March 28, 2023

## Slide 2: Introduction
Finite Element Method
Ron Timothy Gitonga Ndwiga, Esther Mugure Ngugi
LOGO HERE
The Finite Element Method (FEM) is a numerical technique for solving partial differential equations (PDEs) in complex domains.
It is widely used in engineering and physics applications, and provides accurate and efficient solutions to a wide range of problems.
In this presentation, we will discuss the steps to solve a PDE using FEM, and how to implement it using Python and the Matplotlib library.

## Slide 3: What is FEM?
Finite Element Method
Ron Timothy Gitonga Ndwiga, Esther Mugure Ngugi
LOGO HERE
FEM involves dividing a complex domain into small, simple subdomains called elements.
These elements are connected at shared points called nodes, forming a mesh.
The solution to the PDE is approximated by piecewise polynomial functions within each element, and the solution over the entire domain is obtained by assembling the element solutions and solving the resulting system of equations.
The accuracy of the FEM solution depends on the number and size of the elements in the mesh, as well as the order of the polynomial functions used to approximate the solution.

## Slide 4: Applications
Finite Element Method
Ron Timothy Gitonga Ndwiga, Esther Mugure Ngugi
LOGO HERE
FEM is used in various applications, including: Structural Analysis
Fluid Dynamics Electromagnetics Heat Transfer Acoustics

## Slide 5: Steps to Solving a PDE using FEM
Finite Element Method
Ron Timothy Gitonga Ndwiga, Esther Mugure Ngugi
LOGO HERE
The steps to solve a PDE using FEM are:
1
2
3
4
5
Discretize the domain into elements Define the element shape functions
Assemble the stiffness matrix and load vector Apply boundary conditions
Solve the resulting system of equations
Example PDE: Poisson’s equation in 2D
−∇2u(x, y ) = f (x, y )
Here, ∇2 is the Laplacian operator, and u(x, y ) is the unknown function to be solved for. The equation states that the sum of the second partial derivatives of u with respect to x and y equals a given source term f (x, y ). For our specific problem, this equation takes the form:

## Slide 6: Implementing the Finite Element Method in Python
Finite Element Method
Ron Timothy Gitonga Ndwiga, Esther Mugure Ngugi
LOGO HERE
To implement the Finite Element Method in Python, we can use the NumPy and SciPy libraries to perform numerical calculations and linear algebra operations. Here’s an example of how we could solve the Poisson’s equation using FEM in Python:
1
2
3
4
Define the mesh of nodes and elements
Assemble the global stiffness matrix and force vector Apply boundary conditions to the system of equations
Solve the system of equations to obtain the nodal values of the solution

## Slide 7: Conclusion
Finite Element Method
Ron Timothy Gitonga Ndwiga, Esther Mugure Ngugi
LOGO HERE
FEM is a powerful numerical technique for solving PDEs in complex domains. It involves dividing the domain into small subdomains called elements, and approximating the solution as piecewise polynomial functions within each element. The accuracy of the solution depends on the number and size of the elements in the mesh, as well as the